## Slide 1
CDFW - Sites 60 day Evaluation
Initial Meeting
            May 30, 2019
Sites

## Slide 2: Agenda
    Introductions and Purpose
    Project Overview & Updates
    Operations Simulations – Hydrology & Tools
    Operations Results
    Tools
    Next Steps

## Slide 3: Purpose of the 60-day
    Guide the Authority to increase the clarity of the Project Description and supporting analyses for an affordable project capable of providing meaningful water supply and dedicated ecosystem benefits looking toward
    Final EIR/EIS
    Permit applications

## Slide 4: Anticipated Issues
    Diversion rate and timing
    Trigger values
    Floodplain and Bypass habitat
    Coldwater pool development and release
    Flow stability supply development and release effects
    Flow-mortality analysis and scientific basis
    Sites Reservoir water quality and release effects
    Sediment management
    Delta Outflow management and effects

## Slide 5: Regional Map
5
Notes: Sites is a sustainable surface water project that uses available facilities and adds storage and conveyance to:
improve conditions for chinook salmon in drier years and delta smelt in all late-summers and falls
Increases deliveries to wildlife refuges in dry years
Eliminates floods that closed I-5
Increases water supplies for families, farms and business in drier years
Is more effective as climate changes occurs

## Slide 6: Project Facilities
Maxwell
Sacramento River
Pumping Plants
6
Notes: If 1.8 MAF is not affordable (permit conditions or reduced participation), purse a smaller-sized project. Environmental Analysis has been done on a 1.3 MAF reservoir (with same size facilities).
If smaller-sized project is not affordable (permit conditions or reduced participation), pursue the Intertie between the T-C Canal and GCID Canal. Concept has been previously studied. Expect only Sacramento Valley participation, which would likely reduce the size and cost. With an intertie, an asset has been created.

## Slide 7: Sites Project Analytical Modeling Framework
Hydrology &
System Operations
CALSIM II Merged Model, USRDOM (daily Model)
Water supply impacts, river flows, exports, storage
Salinity (EC, Cl, TDS, Br) and fingerprinting (EC, volume)
Delta Hydrodynamics
DSM2-HYDRO
Delta Water Quality
DSM2-QUAL
Reservoir/River Temp
Reclamation HEC5Q
Power
LTGEN, SWP Power, NODOS Power,
Economics
SWAP,
CWEST, LCRBWQM/SBWQM
Delta channel flows, stages, velocities
Reservoir, River temperatures
Climate Change Modified Hydrology
Sea Level Rise
VIC, ANN
Fisheries
Early Lifstage Mortality, SALMOD,
WRCLCM (IOS), OBAN
Quantification of Economic Benefits
Net Generation and Use
Survival, Potential Production, Population

## Slide 14: Daily Operations Model Watershed

## Slide 15
Chart: Storage (TAF, End-of-September)
| 1924 | 1929 | 1931 | 1933 | 1934 | 1939 | 1977 | 1988 | 1991 | 1992 | 2014 | 2015
System Storage Without Sites | 2175.3326 | 2953.9662 | 2530.7143 | 2999.3503 | 2604.2385 | 2632.5248 | 1323.7783 | 2817.4485 | 2400.0215 | 2191.5653 | 2577.947 | 2833.426
Level at which DWR and Reclamation submitted a Temporary Urgency Change Petition on January 29, 2014
Combined Storage During Extremely Dry Conditions (Shasta, Oroville, Folsom)
15
Notes: Click for red line. Then, click for Sites (green bars)
Fritz:
▪ Blue incorporates today’s environmental compliance obligations and level of water demand onto the historic hydrology associated with past droughts to estimate the end-of year storage in Shasta, Oroville, & Folsom
▪ Red line shows when the Projects pursued the TUCP process
▪ The green is how much water Sites could have diverted under current environmental compliance obligations and ensuring that senior water right holders demands were met first.
When the next drought comes, Sites will “move the needle” to ensure there is additional water for both the environment and for people

## Slide 16
Chart: Storage (TAF, End-of-September)
| 1924 | 1929 | 1931 | 1933 | 1934 | 1939 | 1977 | 1988 | 1991 | 1992 | 2014 | 2015
System Storage Without Sites | 2175.3326 | 2953.9662 | 2530.7143 | 2999.3503 | 2604.2385 | 2632.5248 | 1323.7783 | 2817.4485 | 2400.0215 | 2191.5653 | 2577.947 | 2833.426
System Storage With Sites | 788.7905 | 711.6258 | 541.4655 | 551.0776 | 579.1276 | 1299.9613 | 459.1621 | 572.1317 | 669.9093 | 550.0679 | 710 | 710
Level at which DWR and Reclamation submitted a Temporary Urgency Change Petition on January 29, 2014
Combined Storage During Extremely Dry Conditions (Shasta, Oroville, Folsom, & Sites)
16
Notes: Benefits of Sites
Not able to address all years, but definitely can move the needle

## Slide 17
SALMOD Results
(Longterm)
17
 | 2030 |  |  | 2070 |  | 
Sacramento River Chinook Runs | Without Sites | Sites Increment | % Change | Without Sites | Sites Increment | % Change
Winter | 1,996,967 | 68,269 | 3.4 % | 1,818,783 | 109,752 | 6.0%
Spring | 437,648 | 4,147 | 0.9% | 357,458 | 17,520 | 4.9%
Fall | 17,896,789 | 226,190 | 1.3% | 15,507,733 | 623,264 | 4.0%
Late-Fall | 2,892,264 | 20,442 | 0.7% | 2,744,016 | 95,108 | 3.5%
All Runs | 23,223,668 | 319,047 | 1.4% | 20,427,989 | 845,644 | 4.1%

## Slide 18
SALMOD Results
(Incremental Change - Dry Years)
18
 | Dry Years |  |  | Critical Years |  | 
Sacramento River Chinook Runs | Current | 2030 | 2070 | Current | 2030 | 2070
Winter | 2.3% | 2.6% | 6.1 % | 2.3% | 14.8% | 66.7%
Spring | 1.3% | 0.3% | 6.3% | 20.2% | 6.0% | 64.8%
Fall | 1.6% | 0.6% | 7.0% | 3.9% | 3.1% | 11.3%
Late-Fall | 2.3% | 1.2% | 1.6% | 4.4% | 1.6% | 21.2%

## Slide 19
Flow Stability Results
19
Flow Stabilization (Percent change in Average December-February flow increases from Keswick Dam) |  | 
Hydrologic Condition | 2030 | 2070
Long-term | 2.5% | 1.7%
Below Normal | 3.8% | 3.9%
Dry | 11.9% | 6.1%
Critical | 4.2% | 7.9%

## Slide 20
OBAN Results
20
Long-term Average Escapement for Winter-Run Chinook Salmon (1971-2002) |  |  | 
 | Current | 2030 | 2070
Without Sites | 3997 | 2813 | 2258
Increment with Sites | 283 (7.1%) | 70 (2.5%) | 240 (10%.6)
Sites Increment with Flow-Mortality Correction | 264 (6.6% | 58 (2.1%) | 228 (10.1%)

## Slide 21
Next Steps?
Topics, Date